## Slide 1
National Electrification Planning for Myanmar (NEP):
National Geospatial, Least-Cost Electrification Plan
Columbia University, Earth Institute
Vijay Modi, Director
Edwin Adkins, Presenter
Sustainable Engineering Laboratory
With thanks to: Resources and Environment Myanmar (Yangon)

## Slide 2: Approach
+
Approach
Collect input data
  populated places, MV grid lines, and numerous modeling parameters
Use algorithm to plan least-cost electrification system
  grid, mini-grid, off-grid (solar home systems)
Plan the sequence of grid roll-out in phases
Objective: Least-cost electrification planning ensures that we maximize the results with limited resources. Sequencing tells where and when to prioritize the work.
Populated places
Grid lines
Select least-cost technology
Plan Roll-Out
(5 Phases)
Notes: Need work

## Slide 3: Part 1: Methodology

## Slide 4: Population Data Sources
Ministry of Livestock, Fisheries and Rural Development (DRD)
  Village Level Population Data, 2001
Ministry of Home Affairs, General Administration Department (GAD)
  Additional population data for villages, cities and towns (2013)
Central Statistical Organization (CSO)
  Rural and Urban Total Population and growth rates
Myanmar Information Management Unit (MIMU)
  Geo-location of all villages by State (but no population data)
When combined these sources provided:
  64,000 points for villages
  300 points for cities and towns
  rural and urban growth rates, by year, for each state / region

## Slide 5: Important Caveat
The source data for populated places has an inherent uncertainty, and the upcoming census data will help improve the modeling results in the future updates.
This uncertainty limits the precision of any analysis, and values in this report should be regarded as the best estimates given this underlying data limitation.

## Slide 6: Obtaining and Preparing Population Data
Data tables were collected in digital and hardcopy from DRD, GAD, MIMU
Population Growth Rates were taken from CSO publication (2011)
Together these created one geo-located dataset with villages, towns and cities with population for a common year (2011)
DRD
GAD
CSO
MIMU

## Slide 7
ESE and YESB supplied hundreds of maps in jpeg, pdf and other formats for state, district and township level MV lines. (samples above for Bago)
These were geo-referenced and digitized to create GIS files.
(Bago Region MV file created by Resources and Environment Myanmar, Yangon).
Medium Voltage (MV) grid lines

## Slide 8: Model Parameters
  ESE provided:
    Costs for LV (400 V) and MV (11kV, 33 kV) grid lines
      ~US$20,000-22,000 per km
    Sizes and costs of generators and transformers used
    Cost of diesel fuel
      4,400 – 4,900 kyat (US$1.10 - 1.22/liter) varying by state
    Electricity demands for residential sector (households)
      1,000 kWh per Household, per year
  Castalia estimated the future “bus-bar” cost of power:
    130 kyat (13 US cents) per kWh
  More than 70 other parameters were obtained from discussion with utilities and local investigation, in some cases compared with international values.

## Slide 9: Using software to plan a “least-cost” electricity system
Our model receives inputs described previously:
  Settlements, MV grid lines, and many parameters
… and an algorithm estimates demand and all costs (initial and recurring), and identifies which settlements will most cost-effectively be served by different electrification technologies over the long term:
  grid connection,
  mini-grids (such as diesel or hybrid) or
  off-grid (such as solar home systems).
Settlements
Existing Grid
Model Results

## Slide 10: Final Step: Sequenced roll-out
MV grid extension is divided into 5 equal phases.
Sequencing prioritizes new lines that serve the highest demands with the shortest MV line extension.
Earlier Phases (1 & 2) reach larger, closely spaced settlements.
Later Phases (4 & 5) reach the smallest, most remote settlements.

## Slide 11: Part 2: Results for Myanmar

## Slide 12: Two-pronged Approach: Grid and Off-grid Rollout Plan
Grid extension will reach some states later in grid roll-out, and these connections will cost substantially more per household
For those areas where grid will arrive late, an off-grid “pre-electrification” option can provide non-grid electricity service in the short- and medium-term
Over the long-term, grid extension is the most cost-effective option for the overwhelming majority of households

## Slide 13
20
Note: This map shows all settlement points the same size (regardless of population), overstating electrification with non-grid options (mini-grid and off-grid / solar home systems)
Least-Cost Recommendation for 2030
By 2030, the majority is grid connections
This will be 7.2 million households
Total cost is estimated at US $5.8 billion (US$800 per connection, average)
This will be in addition to investments needed for generation & transmission

## Slide 14: Number of households (estimated in each state) that will need to be connected
Caution: estimates and not primary census data. So +/- 10% variation would be not unexpected

## Slide 15: Grid is recommended (long-term) for all but the smallest villages
Off-grid (solar home systems) and mini-grids are recommended only for the smallest settlements
Number of households per village

## Slide 16
2.5-3.0 GW of new generation capacity will be needed only for modest, residential needs
More will certainly be needed for commercial, industrial, and other demands.
This is approximately doubling current generation (~2.7 GW)
State | New Proposed Connections Capacity (MW) | 
Ayeyarwady | 1,082,000 | 395
Bago | 688,000 | 251
Chin | 112,000 | 41
Kachin | 115,000 | 42
Kayah | 27,000 | 10
Kayin | 379,000 | 139
Magway | 811,000 | 296
Mandalay | 722,000 | 264
Mon | 258,000 | 94
Nyapitaw | 98,000 | 36
Rakhine | 977,000 | 357
Sagaing | 909,000 | 332
Shan | 504,000 | 184
Tanintharyi | 325,000 | 119
Yangon | 208,000 | 76
Total | 7,216,000 | 2,636
Generation Capacity Needs

## Slide 17: Medium-Voltage (MV) Extension
Chart: Length of MV Required by States
| Ayeyarwady | Bago | Chin | Kachin | Kayah | Kayin | Magway | Mandalay | Mon | Nyapitaw | Rakhine | Sagaing | Shan | Tanintharyi | Yangon
MV Required | 8324.168 | 4674.064 | 3195.316 | 1983.608 | 556.413 | 2936.903 | 6418.632 | 4437.317 | 1301.057 | 666.906 | 4971.491 | 7778.895 | 10510.511 | 2349.171 | 1594.333
The amount of new MV line needed varies greatly by state / region.
Shan state is estimated to need the most new MV line overall and the most per household.

## Slide 18: 2) Grid extension will reach some states later in grid roll-out, and these connections will cost substantially more per household (This applies primarily to Chin, Shan, Kachin and Kayah, and to a lesser extent Kayin, Sagaing, Tanintharyi.)

## Slide 19
Recommended sequencing of Grid Roll-out proceeds from low-cost to high-cost connections
Dense areas require less MV per connection and will be connected first
Remote communities require more and will be connected later
Chin, Shan, Kachin and Kayah have highest cost per connection, thus to be connected in the final phases
Connected earlier
Connected later

## Slide 20
Phasing by equal MV distance
MV Line Cost Rises Dramatically in the Final Phase
Grid roll-out has five phases, each with equal MV distance.
Most households will be connected in the initial phases at lower cost per connection.
In later phases, as grid reaches remote communities, the length of MV line needed per household increases.
The MV line investment rises dramatically in Phase 5 raising connection costs as well.

## Slide 21: The most MV line per household, and the highest costs of grid extension, are estimated in 4 states: Chin, Kachin, Kayah, Shan (and somewhat in Kayin, Sagaing and Tanintharyi)
Meters MV per HH

## Slide 22: 3) For those areas where grid will arrive late, a “pre-electrification” option can provide non-grid electricity service in the short term

## Slide 23
Remote areas will be reached in the latest phases (perhaps waiting for 10-15 years)
Other technologies can meet needs in the short term. We call this “pre-electrification”
Pre-electrification options would be lower service standards for basic needs
  Initial costs are lower than grid (~20-50% less)
  More important, roll-out would be faster
“Off-grid Pre-electrification”: the need

## Slide 24
Consider the last 3-4% of settlements for pre-electrification
  -- 5,000 communities
  -- 250,000 households
Pre-electrification communities shown in purple
Shan, Chin, Kayah and Kachin States represent major areas for pre-electrification
Which system is best (solar home system versus mini-grid) depends on the size of the settlement
Recommendations for a Off-grid, Pre-electrification Plan

## Slide 25: Important Caveat
The issue of how many households and communities should be targeted for “pre-electrification” is more of a policy decision than a technical decision.
The technical geo-spatial analysis presented here describes how costs increase for electrification of communities due to high MV costs per household.
However, it does not determine the cost limit above which households should be targeted for “pre-electrification” rather than grid.

## Slide 26
Solar home systems
  for smaller settlements (<50 HHs)
  may provide 75-175 kWh/yr for lighting/ICT/TV
  US $400-500 / household system
    (These are international prices. Local prices may be lower, and quality can vary.)
Mini-grids
  solar, hybrid, diesel, or micro-hydro where available
  typically best for larger settlements (>50 HHs)
  200-250 kWh/yr : lighting/ICT/TV & fan/small fridge
  US$1,400/HH
  Cost is somewhat high, but saves on distribution investment later if built to grid standard
“Pre-electrification” Technology Options

## Slide 27: One pre-electrification option-- targeting 250,000 HHs in the first 10 years
Solar home systems for ~95,000 HHs in small villages (<50 HHs)
Mini-grids for ~155,000 HHs in larger villages (>50 HHs)
Number of households per village

## Slide 28: 250,000 “pre-electrification” households by State / Region

## Slide 29: Pre-electrification Cost summary
 |  | 250K
Households targeted for SHS |  | 93,000
Total Initial Costs |  | $47,500,000
HHs targeted for mini-grids |  | 156,000
Total Initial Costs |  | $219,000,000
Grand Total: Households |  | 250,000
Grand Total: Costs |  | $266,500,000
Overall Ave per HH Costs |  | $1,070
Notes: comments: round numbers to million $.